Scrutineering Form

______________    ______________

Name of Boat	Racing Number

Racing Class		_____________

Racing Number 	_____________

Colour of hull	  	_____________

Colour of deck   	_____________

Length  		_____________

Make/Model		_____________

Designer		_____________

Mono/Cat		_____________

Yr of Manufacture	_____________

Material	             	______________

Inboard/Outboard	______________

No of engines    	______________

Make/Model 		______________

Total Cubic Cap 	______________

Total Rated HP  	______________

No of crew		______________

Fuel Capacity    	______________

HULL

- DECK

- Check for looseness from frames 	_____

- Check for loose fiberglass 		_____

- Check for cracks 			_____

- Check for loose trim 		_____

- BOTTOM

- Check for loose fiberglass 		_____

- Check for cracks 			_____

- Check location and type of drains 	_____

- FRAMES

- Check for integrity of all joints 	_____

- Check fasteners 			_____

- Check for cracks			_____

COCKPIT

- MAIN STRUCTURE

- Check for main structural integrity 	_____

- Check for loose upholstery, exposed

areas that may hinder riding crew 	_____

- Check seat/bolster adequately

attached to boat 			_____

- Check for adequate leg clearance 	_____

- Check for installation of radio 	_____

- Compass mounted securely              _____

- GPS mounted securely                      _____

- CANOPY

- Check for securely fastened 	_____

- Check for cracks or breaks 		_____

- If using aircraft canopy, which

model _____________________________

- Check for opening mechanism,

hinge, latch per LAVIN standards

and minimums 			_____

- Check for cockpit opening with

canopy open to LAVIN standards

and minimums 			_____

- Check driver's head clearance	_____

- Check for inspection sticker on air

bottles, check air mask 		_____

- UPHOLSTERY

- Is upholstery securely attached 	_____

- Check for upholstery covering sharp

edges				_____

- STEERING WHEEL

- Check for rust 			_____

- Check for loose cover 		_____

- Check for sharp edges 		_____

- Check for proper attachment - check splines/taper, keyway, key attaching

bolts, locktited bolts, coller-pull

release mechanism 			_____

- FIRE EXTINGUISHERS

- Check for bottles securely mounted 	_____

- Check for cables free and operable,

or electric 				_____

- Check extinguisher fully charged	_____

- THROTTLE

- Check for secure attachment 	_____

- Check for smooth and free action 	_____

- Check that spring returns throttle to

off position 				_____

- Check cable is well secured 	_____

- FOOT BRACE

A. Check structure, mounting 		_____

- DASHBOARD

- Check adequate drivers leg

clearance, padding on underside of

dash 				_____

- Check for secure attachment 	_____

- Check for secure sub structure 	_____

- SHUT-OFF DEVICES/SYSTEMS

- Check that systems can be easily

activated & where required are

properly

marked as described in rule book 	_____

- Check that system activation will

ground ignition 			_____

- MASTER ELECTRICAL SWITCH

- Check for easy access for crew 	_____

- Check for secure mounting 		_____

- CIRCUIT BREAKERS (OPTIONAL, RECOMMENDED)

- Examples: Instruments l5 Amp,

Fuel Pump 20 Amp, Water pump

20 Amp 				_____

SWITCHES

- Check for free action		_____

- Check for secure attachment 	_____

- WIRING

- Check for corrosion 			_____

- Check for tight wire lugs 		_____

- Check for chafed or cut wires 	_____

- Check for wire bundles tied off 	_____

- DRIVER RESTRAINT SYSTEM

- Check straps and buckle 		_____

- Check straps for wear or fraying

and date stamped 			_____

- Check buckle for rust, smooth

operation 				_____

- Check for adequate attachment

to hull 				_____

- PLUMBING

- Check for frayed hoses 		_____

- Check for corrosion on ends (pull

test)				_____

- Check for loose fittings and ends 	_____

- Check for hose bundles tied off	_____

- ENGINE STRINGERS/INTERNAL STRUCTURE

- Check for secure engine & gearbox attachments, wear or elongation of

bolt holes 				_____

- Check for internal structural damage

due to heat, oil, or explosion 	_____

- COWLING

- Check attachments for removable

cowling 				_____

- Check attachments for engine

cover/covers 			_____

STEERING SYSTEM

- SYSTEM

- Check bolt holes for elongation	_____

- Check bearings/bushings for

clearance and freedom of movement_____

- Check transom attachment 		_____

- Check fittings and tubes for cracks 	_____

- Check hoses and fittings for

corrosion and fraying 		_____

- Check for NO brazed fittings or

joints			 	_____

- ROD ENDS

- Check for loose ball 		_____

- Check threads for fit and rust 	_____

- Check nuts and bolts 		_____

- Check tie rods for rust and cracks 	_____

CUMPULSORY SAFETY EQUIPMENT

- Life Jacket for each occupant

- Helmet for each occupant, orange or red in colour with racers name & blood type clearly visible on same.

- Hand bilge pump or bailer and electrical bilge pump

- Anchor or grapnel

- 65 meters (200 ft) of rope at least 1/2” (5/8” C & M class) diameter

- Water Proof Flash light (2 D Batteries)

- Towing cleat, Sampson post or bow ring

- Approved first aid kit

- Identification, Class designation and number on port & starboard sides of boat and on top of deck to be correct dimensions

- Adequate tool kit including knife & mirror

- Emergency Locator System

- One gallon of drinking water per crew member

I certify that the information contained herein is correct and that I am not knowingly in breach of the Trinidad & Tobago Power Boat Association Racing Rules Regulations.

________________		__________________			____/____/____

Owner/Captain			Name in Block Letters			         Date

----------------------------------------------------------------------------------------------------------

_____________ and the safety equipment as per attached sheet were inspected on

Name of Boat

____/____/____ by _____________ (signed) _____________ (block letters)